## Slide 1: Lowering the Asphalt Production Temperature
www.ammann-group.com

## Slide 2: Our Planet
http://maptd.com/
Notes: This Fascinating view of the earth is a global average of data recorded by the tongue twisting Sea-viewing Wide Field-of-view-Sensor (SeaWiFs) over the entirety of its 13 year operational history – 1996-2010.
During its lifespan this sensor on GeoEye’s OrbView 2 satellite measured worldwide levels of chlorophyll – the green pigment which allows plants to obtain energy from light. As NASA Earth Observatory explains, at sea the colours in the map represent areas where phytoplankton is most common, on land the the density of vegetation:
An NDVI of zero means no green plants and a high value (0.8 or 0.9) is a thick canopy of green leaves.
As to why monitoring phytoplankton levels is really important:
It’s the blooming and die-off of the phytoplankton that form the center of the oceanic food web…a direct indicator of the seas’ ability to support life.
NASA Earth Observatory image by Jesse Allen, using data provided courtesy of the Ocean Color Web team. Caption by Patrick Lynch and Mike Carlowicz.

## Slide 3: CO2 emission per ton of Asphalt in Australia
Production of raw
materials and energy
Australia, model calculation, Transport not considered (5-15 kg CO2 per t of Asphalt)
Indirect Emissions
30 kg CO2
0
5
10
15
20
Aggregates
Bitumen
Electricity
kg CO2 per t of Asphalt
Bitumen Storage
Logistics
Dryer
On the Mixing Plant
20 kg CO2
Direct Emissions
Asphalt- Recycling
Lower mixing Temp.
Less moisture content
Total 50 kg CO2

## Slide 4: Lower Temperature reduces Energy Consumption
0°C
50°C
100°C
150°C
200°C
Heating & Drying
Heating
Energy Consumption per ton asphalt
Cold Asphalt
Half Warm Asphalt
Warm Asphalt
Hot
Asphalt
Technology Trend = Lower Temperatures
115°C
180°C
1.5 kg Oil
CMC
Foam
Additives
HMA
Notes: Die Zukunft liegt in der niedrigen Temperatur. Sicher nicht höher!

## Slide 5: Loading of Hot Mix and Ammann Warm Foam
Temperature reduction of 10°C reduces fume by approximately 50%.
50 °C cooler = - 80% emissions.
Hot-Mix
Foam Asphalt
Emissions during loading
180 °C
~ No Emissions
115°C

## Slide 6: Lower Emissions at the Construction Site
Emission during paving
165 °C
No emissions
100°C
Notes: Emissions of the asphalt not only occur on the asphalt mixing plant, but also on the construction site during paving. On the construction side as well, the emissions can be reduced dramatically. This reduction in emissions increases the conditions of the paving workers significantly. You even don’t smell the asphalt on the site anymore.

## Slide 7: Foaming: Same Viscosity at Lower Temperature
Viscosity of Bitumen
Temperature [°C] and / or Time
0
Bitumen B 50/70
Foamed Bitumen
Schematic Illustration
Bitumen with Wax

## Slide 8: Verdichtungsfenster – Abhängig von der Technologie
Time
Viskosität des Bitumens
Schaumbitumen
Standard Bitumen
Lagerung
Mischen
Transport
Einbau &
Verdichtung
Verkehr
Abkühlen
Bitumen mit Wachs
Früheres Ende
Schematic Illustration

## Slide 9: Bitumen Foaming
Hot Bitumen
160°C
+
Cold Water
2 - 4%
=
Bitumen Foam
+
Fine Distribution
1 litre
0.03 litre
20 litres
5 % of asphalt
0.15% of asphalt
water: 0.05% of asphalt

## Slide 10: Ammann Foam Generator – Basic Principle
Static Mixer
Hot Bitumen
Foaming water
2-4% of bitumen
(0.1-0.2% of asphalt)
Spraying nozzles
High pressure (water & bitumen)
Foamed bitumen
Mixer
Notes: The Ammann Foam Generator is the core components for producing low temperature asphalt with foamed bitumen. Hot bitumen is pumped into the foam generator. Cold water is injected and mixed with the hot bitumen. The mixing of water and bitumen takes place under high pressure. The water/bitumen mixture is pressed through the nozzles and after it has left the foam generator, the water expands and the foam is generated.

## Slide 11: Ammann Foam – Pure Foam Bitumen - 100 – 120 °C
Notes: Wichtig: Gut arbeitender Mischer, angepasste Mischsequenz

## Slide 12: Ammann Warm Foam - Switzerland 2009
Bitumen
Water
Mixer
Bitumen & Water
Sample
Taking

## Slide 13: Ammann Warm Foam - Switzerland 2009

## Slide 14: Foam Asphalt - Switzerland – 2012 – 115°C

## Slide 15: Low Temperature Asphalt Promotion
www.foamasphalt.info

## Slide 16: Low Temperature Asphalt: All Parties have to Contribute
National and state road authorities
Supporting new technologies
Road construction companies
Investing in new technologies
Ammann
Developing new technologies

## Slide 17: Productivity Partnership for a Lifetime
www.ammann-group.com